## Slide 1: Inspect Gas Cylinder Straps
EHS Reps or designee--Please inspect the cylinder straps in your lab when you change cylinders and when you prepare for level 2 inspections.
Replace straps if:
  There is a cut/tear of any size or Fraying
  Tension buckle slips
Refer to following photos of these issues

## Slide 2: Strap in a MIT lab tore like paper during cylinder change

## Slide 3: Replace strap if you find
Cut/Tear--Any size
Fraying
Excessive wear, webbing is thinning

## Slide 4: Strap with a small tear
Check straps when you change cylinders
Bend the strap, look at the edges, and run your hand along the entire strap

## Slide 5: How to determine if a strap is safe
Pull the strap
if the tension spring slips, replace the strap
if the strap stays taut, strap is OK.

## Slide 6: Inspect the tension spring for corrosion and loss of tension
Rusty handle/ spring is OK
Torn cotton blend belt no spring